CSE 233 Lab-4
Mehmet Hüseyin YILDIZ
200104004095

Why Thevenin and Norton Theorems are used in the circuits ?

Thevenin and Norton Theorems used circuits to simplify. If we don’t want to calculate and deal with a complex part of the circuit. We apply Thevenin and Norton theorems.

How Norton current and Thevenin voltage are found in a circuit ?

We find the R equivalent between nodes by making all independent sources off. We calculate or measure the voltage between 2 open nodes. This is thevenin voltage. Then calculate current using voltage or mesaure current between 2 open nodes. This is norton current.

RL for the maximum power transfer is 3.3k ohm.

VTH

RTH (3.3k ohm)

Thevenin Equivalent Circuit

Norton Equivalent Circuit

IN Norton short circuit current (equivalent to current in norton circuit)

RL = 0.1RTh

RL = 0.1RTh

RL = 10RTh

Load Res	Meas / IRL / (mA)	Meas / VRL / (V)	Meas / PRL / (mW)	Meas / PRth / (mW)	Calc / IRL / (mA)	Calc / VRL / (V)	Calc / PRL / (mW)	Calc / PRth / (mW)
RL = 0.1RTh					2.204	0.727	1.6	16
RL = RTh					1.212	4	4.848	4.848
RL = 10RTh					0.220386	7.273	1.6	0.16